## Slide 1
DISCUSSION PURPOSE ONLY
Bio-Fuel introduction in Japan from voluntary to mandatory

## Slide 2
DISCUSSION PURPOSE ONLY
１.Introduction
2011FY～ Mandatory introduction of bio-ethanol* based on the
“New Law” started
* either ETBE or direct blend
Nov.2010 The details of New Law were announced
This obligation is imposed on oil refining companies whose gasoline production exceed 600kkl/y.
2007-2010 ETBE introduction in voluntary basis
Jul.2009 Establishment of the “New Law”*
* The Law of Sophisticated Methods of Energy Supply Structure

## Slide 3
○ The Strategic Energy Plan of Japan stipulates: “(The usage of biofuel) shall be targeted for introduction at a level equivalent to 3% or more of gasoline nationwide by 2020, after the implementation of sustainability standards for reductions in greenhouse gases under the LCA (Life Cycle Assessment), and, in conjunction with these standards, ensuring economic viability, sufficient greenhouse gas reduction, and stable supply.”
○ The regulation state that, of this amount, a target for the bioethanol blended with the gasoline supply from oil refiners should be established, and that the regulation will consider the effective implementation of bioethanol from an LCA perspective.
Basic concept
＜ Usage targets＞
○ With regard to the use of automotive fuel consisting of bioethanol blended with gasoline, the aggregate target amount of bioethanol use by oil refiners for the seven years from fiscal 2011 through fiscal 2017 of each year shall be as listed in the following chart.
○ Oil refiners shall annually use biofuel equivalents in amounts obtained through the following equation.
Note: Implement flexible measures (banking, borrowing, etc.) in order to ensure achievement of enterprise usage targets
○ In terms of LCA-based greenhouse gas emissions, bioethanol procured shall be less than 50% of gasoline. In addition, avoidance of competition with the food supply, and ensuring biodiversity, shall be taken into account when conducting procurement activities.
＜ Measures that should be systematically addressed by enterprises＞
○Oil refiners should strive to promote and implement developments of technology use, such as grass and wood cellulose, or algae in the context of biofuel production.
○In order to promote bioethanol use, oil refiners shall strive to establish and to renovate facilities for processing bioethanol.
FY2011 | FY2012 | FY2013 | FY2014 | FY2015 | FY2016 | FY2017
210,000 KL | 210,000 KL | 260,000 KL | 320,000 KL | 380,000 KL | 440,000 KL | 500,000 KL
（ Unit: Crude oil equivalent）
Gasoline supplied domestically by that enterprise 2 fiscal years previous to the present year
Total domestic supply of gasoline by all enterprise 2 fiscal years previous to the present year
Enterprise usage target ＝
２.Regulation relating to the use of non-fossil energy sources by oil refiners
Total amount of
× above bioethanol
usage target
Details of Regulation(main points)
DISCUSSION PURPOSE ONLY

## Slide 4
DISCUSSION PURPOSE ONLY
３．Target volume
Target volume start to increase from 2013 towards 2017
2007FY | 2010FY |  | 2011ＦＹ | 2012ＦＹ | 2013ＦＹ | 2014ＦＹ | 2015ＦＹ | 2016ＦＹ | 2017ＦＹ
 |  |  | 2011ＦＹ | 2012ＦＹ | 2013ＦＹ | 2014ＦＹ | 2015ＦＹ | 2016ＦＹ | 2017ＦＹ
 | as Crude |  | 210 | 210 | 260 | 320 | 380 | 440 | 500
 | as Ethanol |  | 346 | 346 | 428 | 527 | 626 | 725 | 824
 | as ETBE |  | 817 | 817 | 1011 | 1244 | 1478 | 1711 | 1944
Mandatory
Voluntary
Unit:1000kl

## Slide 5
DISCUSSION PURPOSE ONLY
○ More than 50% reduction required
(compared to conventional fossil fuel)
４. Sustainability Standard
(Required condition for raw material ethanol)
１) GHG reduction
○ Boundary of GHG calculation
Objects of footprint calculation
・Direct Land Use Change
・Crop Production
・Feedstock transport
・Conversion
・Liquid fuel transport and storage
Bio-ethanol for Japan must achieve GHG reduction target which is set and calculated through Life Cycle Assessment

## Slide 6
○ LCA (Life Cycle Assessment) is a tool to evaluate environmental impacts of a product or service through its life cycle (from production, use to disposal). Environmental impacts include energy, material resources and environmental burden caused (such as CO2, SOx, NOx in case of air emissions). LCA also takes into account of production and disposal of raw materials and production facilities which are used to manufacture that product.
○ In assessing biofuel’s life cycle CO2 emissions, the whole processes from raw material cultivation to final fuel use are evaluated.
5
２)Calculation of GHG emissions based on LCA
Raw material cultivation
・Machine engine
・Fertilizer input, etc
Raw material transport
・Fuel consumption of trucks, etc
Fuel production
・Pretreatment
・Conversion process, etc
Fuel transport
・Sea transport
・Domestic transport, etc
Energy used and environmental burden caused in producing fossil fuels, chemicals, etc
Energy used and environmental burden caused in constructing and demolishing facilities, etc
Consumption
Example of process from biofuel production to consumption
(Elements which have little impacts such as facility construction may be excluded. )
DISCUSSION PURPOSE ONLY
Notes: 5

## Slide 7
３)Life Cycle Assessment (LCA)
○ Regarding biofuel as a global warming countermeasure, lifecycle emissions of biofuel (reduction rate compared to fossil fuel) is one of the most important sustainability standards of biofuel.
○ CO2 emission at the time of the combustion of biofuel is regarded to be zero due to carbon neutral characteristics. However, GHG are emitted at the time of raw material cultivation, fuel production and so on. Therefore, lifecycle GHG emissions should be calculated. If lifecycle GHG emissions of biofuel are not smaller than those of fossil fuel replaced, biofuel cannot function as a global warming countermeasure.
○ If use of biofuel will become an obligation as a global warming countermeasure in the future, it is indispensable to verify that the biofuel used has GHG emissions reduction effect.
○ In biofuel policies in other countries such as EU Renewable Directive and US RFS (Renewable Fuel Standard) , evaluation of lifecycle GHG emissions of biofuels is mandatory. It is also required to meet the certain reduction rate compared to fossil fuel.
Comparative example of the lifecycle GHG emissions
Causes of emissions in each stage of biofuel and gasoline are as follows.
 | Biofuel | Gasoline
Raw material production | Raw material cultivation | Crude-oil mining
Raw material transport | Raw material transport | Crude-oil transport
Fuel production | Biofuel production | Crude-oil refining
Fuel transport | Biofuel transport | Gasoline transport
Consumption | 0（Carbon-free） | Gasoline consumption
Only the Biofuel B has the GHG emissions reduction effect in the left graph.
排出増
※効果なし
排出減
※効果有り
×
Biofuel A
Lifecycle GHG emissions
Biofuel B
Biofuel A
Gasoline
Fuel use
Fuel transport
Fuel production
Raw material transport
Raw material cultivation
×
Increased emissions
※Not effective
Reduced
emissions
※ Effective
DISCUSSION PURPOSE ONLY
Notes: 6

## Slide 8
４)Lifecycle CO2 emissions reduction effects of bio-ethanol used in Japan
Note1: High-yield rice 1 shows the estimation result for rice grown in rice field with altering water management, while high-yield rice 2 shows the one for rice grown in rice field without altering water management.
Note2: Lifecycle GHG emissions of gasoline is estimated to be 81.7gCO2/MJ.
Note3: When biofuels are produced and consumed locally, emissions from fuel transport is counted as zero.
○ Ethanol from Brazilian sugarcane has more than 50% emissions reduction effect in case land use change does not occur. On the other hand, based on the currently available data, in case of developing new farmland by converting grassland into sugarcane field, it is estimated to emit less CO2 than gasoline but does not meet the standard due to emissions from land use change.
○ Regarding domestic ethanol, ethanol from sugar beet and construction and demolition waste has more than 50% emissions reduction effect. Ethanol from high-yield rice grown in rice field without altering water management has 30% emissions reduction effect. Ethanol from molasses has 32% emissions reduction effect.
Chart: g-CO2/MJ
| Molasses | Construction and demolition waste | Sugar beet | Off-spec wheat | MA rice | High-yield rice 2 | High-yield rice 1 | Conversion from forest | Conversion from grassland | Existing farmland | Gasoline | Domestic materials （for reference） | Brazilian Sugarcane |
Land use change | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 245 | 37.4 | 0 | 81.7
Raw material cultivation | 0 | 0 | 6.9 | 6.7 | 21.5 | 18.9 | 52.8 | 14.4 | 14.4 | 14.4
Raw material transport | 0 | 1.4 | 4.7 | 0.8 | 0.8 | 0.8 | 0.8 | 1.5 | 1.5 | 1.5
Fuel production | 51.4 | 2.9 | 23.5 | 32.2 | 33.4 | 33.4 | 33.4 | 3 | 3 | 3
Fuel transport | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 13.9 | 13.9 | 13.9
DISCUSSION PURPOSE ONLY
Notes: 7

## Slide 9
DISCUSSION PURPOSE ONLY
５) Food Security
６) Bio-diversification
Oil refining companies should consider the competition with food security. If any problem would be found, they should report the necessary information to the government.
In view of Bio-diversification, oil refining companies should secure that the producers of sugarcane, ethanol and ETBE shall comply with all applicable laws and regulations. If any problem would be found, they should report the necessary information to the government.

## Slide 10
５.Examination of Biofuel Standard
○ In order to secure the safety of cars and environmental suitability, ratio of ethanol is regulated by "the Act on the Quality Control of Gasoline and Other Fuels".
○ The ministerial ordinance was revised and the distribution of E10 was enabled from April 1, 2012.
Before the Revision
Ethanol ： ３％
Oxygen ： １．３％
After the Revision
Ethanol ： １０％
Oxygen ： ３．７％
About the Revision
※Restricted to cars suitable to run on E10.
Background of the Revision
○ Environmental impacts of biofuel are regulated by “ the Act on the Quality Control of Gasoline and Other Fuels“, " the Air Pollution Control Law “ and " the Road Transport Vehicle Act“.
○ As one of the global warming countermeasures, it is expected to expand the use of biofuel. In January 2010, it was decided that METI,MOE and MLIT would start to consider revising laws, and so on, regarding cars suitable to run on E10 and fuel standard.
※１ METI：Ministry of Economy,Trade and Industry ※２ MLIT：Ministry of Land ,Infrastructure,Transport and Tourism ※３ MOE：Ministry of Environment
DISCUSSION PURPOSE ONLY

## Slide 11
６． Tax Exemption for bio-fuel
Gas station
Approved
bio-ethanol etc.
Base gasoline
Gasoline blended
with bio-fuel
Factory
Supply
（ Tax exempted for bio-ethanol etc. ）
・Established in FY2008 → In effective until the end of FY2017
・The bio-gasoline producers can get exemption of gasoline taxes (\53.8/l) for the amount of bio- ethanol or ETBE they blend with base gasoline.
DISCUSSION PURPOSE ONLY
Exemption of gasoline tax・local gasoline tax
Exemption of tariff for imported ETBE
・Established in FY2008 → In effective until the end of FY2013
(We are asking MOF for its extension. )
・The importers can get exemption of tariff (3.1% of the price) for the amount of ETBE they import.
Effects of these tax exemptions
The tax exemptions get the price gap between pure gasoline and bio-gasoline decrease (the price of pure gasoline becomes about equal of that of bio-gasoline).